## Slide 1: NI MultisimTM Basics Schematic Capture & Simulation
Hands-On Training

## Slide 2: What You Need To Get Started
Computer running:
Windows Vista, 7 or 8
Multisim 14.0 or higher (Power Pro)
Ultiboard 14.0 or higher

## Slide 3: File Locations
Root Directory
Exercises <or> Solutions
Multisim
The course installer places the course files in the following location:
Notes:   Replace <Course Name> with the name of the course.

## Slide 4: Getting the Most out of this Course
Experiment with hands-on exercises
Do your best to finish all exercises
If time permits, experiment with different scenarios
Ask questions
Please switch your cell phone to vibrator mode
This course is not designed or intended for teaching:
Electronics theory
SPICE theory
C/Assembly programming

## Slide 5: Contents
Part I
Schematic Capture
Part II
Simulation and Virtual Instruments
Notes:   <Replace text with your lesson titles. Click each smart art, press the left expand icon, and add or remove Lessons as needed. Resize the smart art to fit the actual number of lessons.>

## Slide 6: Course Goals
At the end of this course, you will:
Understand the features of the Multisim user interface
Capture schematics in Multisim
Use interactive simulation to check your design
Use virtual instruments and analyses
Work with basic SPICE syntax
Create custom components
Co-simulate MCU with SPICE

## Slide 7: Part 1 Schematic Capture
The Multisim GUI
Placing components
Placing wires

## Slide 8: What is Multisim?
General purpose EDA tool
Schematic Capture
Simulation
Analyses
Integrated Environment

## Slide 9: Benefits of Integrated Capture & Simulation
Preparation for simulation is as simple as drawing a circuit
Interactive Simulation
Animated Parts
Virtual Instruments
Analyses and Graphs
Effective use of your time!

## Slide 10: The Design Process
Where does Multisim fit in the design flow?

## Slide 11: The Multisim GUI
Organized menus
Quick access toolbars
Design Toolbox
Spreadsheet View
Resizable Workspace
Design Toolbox
Menus
Toolbars
Title Bar
Workspace Area
Spreadsheet View
Instruments Toolbar

## Slide 12: Global Options
Options»Global options
Vary from computer to computer
Stored in the User configuration file
  Change config file and database paths
  Save settings (security copy, backup, simulation data)
  Component placement mode, symbol standard
  Rectangle behavior, mouse wheel behavior, bus wiring
  Message prompts and general simulation settings

## Slide 13: Global Options Simulation tab
Netlist errors action
Default background
Phase shift direction

## Slide 14: Global Options General tab
Selection rectangle
Mouse-wheel behavior
Wiring mode
Localization

## Slide 15: Sheet Properties
Options»Sheet properties
Saved with the design file, if opened in another computer same settings will be used.
Color scheme and display properties
Sheet size
Wire and bus options
Font properties
PCB settings
Visibility status for annotation layers

## Slide 16: Sheet Properties—Sheet visibility tab
Component display properties
Net names display properties
Connectors display properties
Bus entry display properties
Tip: Experiment with changing the display properties of components, keep a balance between good visibility and optimum information display.

## Slide 17: Toolbars and Menus
Organized based in functionality
All toolbar functions found in menus
Right-click toolbar area and toggle toolbars
Customizable (functions, location)
ToolTips
Lock toolbars
Click this section of the
toolbar and drag to relocate.
Menu commands use the
same icon as in the toolbar.

## Slide 18: Customize the Environment
Options»Customize interface
Add/remove functions in toolbars and menus
Create new menus and toolbars
Set shortcut keys
Display properties for toolbars and menus

## Slide 19: Design Toolbox
View»Design Toolbox
Manage various elements in the schematic design
Great tool for medium- and large-complexity designs
Control visibility of annotation layers
Access to the Project View
Design Toolbox toolbar
Design Toolbox tabs

## Slide 20: Design Toolbox Hierarchy tab
Main design file name
MCU workspace
1st page/sheet of design
Hierarchical blocks and
subcircuits of the 1st
sheet
Description box file
Design files
Design blocks
Variants
Description Box
Breadboard (Educational Edition)
MCU Projects
Tip: You can open, close, rename files from the design toolbox. You can also set active variants, active MCU projects and so on.
Variants

## Slide 21: Spreadsheet View
Advanced parameter viewing and editing
Global perspective of objects and properties
Find and select components
Modify component or net properties
Review ERC, Simulation and other results
Tip: You can modify properties for multiple components or nets at once if you use the <SHIFT> or <CTRL> keys for multiple selection.

## Slide 22: Workspace Area
Schematic area
Multiple tabs
Zoom in and out with the mouse wheel (default)
Use View menu to show/hide Grid and Page Border
Design
Workspace Area
Multiple Design Tabs
Page Borders

## Slide 23: Schematic Capture
Multisim offers click-and-place capture mode
Integrated with simulation
Three step process:
Select
Place
Wire
Component Database
In-Use List
Copy
Replace
Rotate
Flip
Multi-section
Automatic
Touching-pins
Dropping

## Slide 24: Components
Symbolic representation of actual parts
All components have a symbol
Many components have a SPICE model and footprint
Capture Area
Simulation Engine
PCB Layout
Symbol
SPICE Model
Footprint

## Slide 25: Components—Properties
Double-click component to:
Change Label, RefDes
Display properties
Value
Faults
Check Pin assignment
Set Variant information
Modify User Field information
In the Value tab, click Edit component in DB to customize the component.
(not for RLC components)

## Slide 26: Components—Edit Component in DB

## Slide 27: Components —Virtual, Real, Layout-only

## Slide 28: Component Database
Tools»Database»Database manager
Three levels:
26,000+ parts (Power Pro edition)
Master database cannot be edited
Database utilities let you merge other users database, or convert a database from a previous version

## Slide 29: Component Database
Corporate database
Share components with colleagues
Located in local disk or network drive
User database
Store your own custom components
If you modify a Master database component, save it into the Corporate or the User database.
Caution: Always backup your Corporate or User database.

## Slide 30: Component Browser
Place»Component
Most common tool to place components.
You can select:
  Database
  Component
  Model
  Footprint
  Search for components
Tip: Right-click anywhere in the workspace and select Place Component to access the Component Browser.

## Slide 31
1
2
3
4
5
6
To place a part, select:
Database
Group
Family
Part
Model
Footprint
You can also:
Search
Obtain datasheet
Print a detail report
View model

## Slide 32: Placing a Component
After selecting a component, a ghost image is attached to the mouse pointer
Click to place
Next RefDes is assigned

## Slide 33: Placing Multi-section Components
Select any section for a new IC
Select C or D to place unused sections of U1
U1, section A and B are already placed, therefore they are not selectable

## Slide 34: Component Toolbar and the In-Use List
Access Master database Groups from the Components toolbar.
Use the In Use List to place another instance of an already placed component.

## Slide 35: Rotating a Component
If already placed
While placing

## Slide 36: Component Search
From the Component Browser, click Search
Use * as a wildcard

## Slide 37: Component Search—Results
Number of components matching search criteria
List of components matching search criteria
Details of component selected
OK will take you to the exact database location

## Slide 38: Nets
Wires are the graphical representation of nets
Modeless (no placing vs. wiring mode)
Mid-air wiring is allowed
Real-time netlist is updated behind the scenes
Easy to change wire connections once placed

## Slide 39: Nets
Multiple wires can make one net or node

## Slide 40: Junction Dots
Junction dots represent a wire connection

## Slide 41: Methods for Wiring—Automatic

## Slide 42: Methods for Wiring—Touching Pins

## Slide 43: Methods for Wiring—Dropping

## Slide 44: Changing Wire Properties
Right-click the wire to access the run-time menu
Change colors, net name font and properties
Delete
Change color
Net properties
(rename)

## Slide 45: Moving Wires

## Slide 46: Re-wiring a Net

## Slide 47: Virtual Wiring
Useful in large designs
Avoids unnecessary wires crossing the schematic
Give a net a name that already exists to create the virtual connection
Use Global or On-page connectors
  Global connectors are visible to the whole design
  On-page connectors are visible to the sheet
  On-page connectors may connect to Global connectors

## Slide 48: Virtual Wiring
My Design
Page X
Page Y

## Slide 49: Lesson 1 Exercises Drawing a Schematic
Set environment preferences
Build and wire a filter circuit
Use different methods for wiring
NI Multisim Basics Exercises
Page 1-1
40 minutes

## Slide 50: Part 2 Simulation and Virtual Instruments
Interactive simulation settings
Virtual instruments
Probes
Circuit Wizards

## Slide 51: Multisim Treats Simulation Differently
Most users are not experts in simulation
User wants the benefit of simulation without having to know the details of SPICE
Netlist is hidden from the main schematic, visible through the SPICE Netlist Viewer
If you want to use advanced SPICE syntax you can, using the Arbitrary SPICE Block or the XSPICE Command Line

## Slide 52: Types of Simulation
Multisim supports the following types of simulation:
  SPICE / XSPICE / PSPICE1
  MCU / RF
Code Modeling
Multisim supports these types of simulation individually as well as together using a unique patented co-simulation technology.
1 Most PSPICE models will work with no problems, if you have a model that doesn’t, contact Support.

## Slide 53: Simulation Models
SPICE model is required to simulate a component
SPICE models are usually available from manufacturers
Accuracy of simulation is directly tied to the complexity of a model
Not all components have a SPICE model
In this course, SPICE models also refer to XSPICE, PSPICE and Code Modeling in most cases.

## Slide 54: Multiple Models Available
Some components offer more than one model
Higher level models simulate more sophisticated or unique effects of the component’s behavior

## Slide 55: Interactive Simulation
Set the simulation to Interactive on the toolbar
Set simulation to Interactive when:
  Using virtual instruments
  Using interactive components
  Viewing results from probes, LEDs and so on

## Slide 56: Observing a Circuit Simulation
Start/Pause/Stop functions
Animated parts
Virtual Instruments
Analyses and Graphs

## Slide 57: Creating Circuits for Simulation
Use parts with models
Add models to part without models
Place sources and ground
Use Circuit Wizards
  555 Timer
  Filter
  Opamp
  CE BJT Amplifier

## Slide 58: Simulation with Real-world Signals
Integrating NI measurement & automation products into the design stage allows real-world stimuli to be used
  Automate testing and validation of design

## Slide 59: LabVIEW and LabVIEW SignalExpress
Use LVM and TDM files with real-world data as input signals
Create and use custom LabVIEW VIs in your circuits
  Input data
  Output data
  Input/Output
Save simulation data as LVM files
Overlay simulation data with measurement results
Verify simulation model accuracy

## Slide 60: Virtual Instruments
Select instruments from the Instruments toolbar
* When the NI ELVISmx driver is installed.
Multimeter | Word Generator | Agilent Function Generator
Function Generator | Logic Analyzer | Agilent Multimeter
Wattmeter | Logic Converter | Agilent Oscilloscope
2-ch Oscilloscope | IV-Analysis | Tektronix Oscilloscope
4-ch Oscilloscope | Distortion Analyzer | Measurement Probe
Bode Plotter | Spectrum Analyzer | LabVIEW Instruments
Frequency Counter | Network Analyzer | ELVISmx Instruments*
 |  | Current Probe

## Slide 61: Virtual Instruments—Front Panel
Double-click instrument icon to open front panel
Set instrument settings just like a real instrument

## Slide 62: Using Instruments in Circuits
Place instruments like any other object
Wire the instrument to the circuit
Configure instrument settings

## Slide 63: Probes
Probes can display:
  Current
  Voltage
  Component power
  Digital state
Probes will appear as an output for the analysis by default
Save space in the schematic

## Slide 64: Lesson 2 Exercises Working with Instruments
Examine the response of the bandpass filter
Learn how to use various instruments
Use probes to examine circuit
Import LabVIEW instrument
NI Multisim Basics Exercises
Page 2-1
40 minutes

## Slide 65: Lesson 10 Educational Features
Component Faults
Ladder Diagrams
Circuit Description Box
Circuit Restrictions
3D ELVIS Virtual Breadboard
Note: The Multisim Education Edition is required for this lesson.

## Slide 66: Component Faults
Access through the Fault tab in the component’s properties window
Use to simulate faults on components
  Open
  Short
  Leakage
Component Faults

## Slide 67: Rated Virtual
Multisim includes rated virtual components
Virtual components
They “blow” if pre-set tolerance is exceeded at simulation
Tolerance is set in the value tab of the properties dialog

## Slide 68: Global and Circuit Restrictions
Hide component faults to force students to find the fault using virtual instruments
Disable access to features that you do not want students to have
Lock subcircuits to create a “black-box” circuit which students need to analyze
Password protect

## Slide 69: Ladder Diagrams
Create interactive ladder diagram logic
Use PLC-like components

## Slide 70: Forms
Used with the Circuit Description Box
Include questions:
  Multiple Choice
  True/False
  Data Entry
  Free Form
Use for assignments or tests
Email circuit file and answers to instructor
Edit»Forms/questions

## Slide 71: 3D Breadboard
Place components in 3D on a virtual breadboard
Practice wiring a breadboard based on a circuit diagram
Component symbols and wires turn green when placed correctly on breadboard

## Slide 72: 3D ELVIS Breadboard
File»New»NI ELVIS I design ... Or NI ELVIS II design
Interact with NI ELVISmx instruments
Place and verify diagram similar as the virtual breadboard

## Slide 73: Lesson 10 Exercises Educational Features
Experiment with the Educational features of Multisim
NI Multisim Basics Exercises
Page 11-1
40 minutes

## Slide 74: Conclusion
Technical Support
Ultiboard Training
Contact Information

## Slide 75: Technical Support
ni.com/multisim
ni.com/ask
NI Circuit Design Suite
Technical Library

## Slide 76: Ultiboard Basics: PCB Layout
1-day Hands-on Training
Learn the next step of the design flow:
PCB Layout
Work with:
Parts
Board Outline
Copper
Copper Areas

## Slide 77: Thank you!
Please complete the course survey and retrieve your course CD.